## Slide 1: What XRISM response files are provided for the Cycle 1 GO proposers?
The XRISM Community Workshop, Jan 17th, 2024 Mihoko Yukita (GSFC/JHU)
The files available for spectral simulations

## Slide 2: What Are Response Files?
E
Flux
S(E) = Source photon flux

## Slide 3: What Are Response Files?
E
Flux
E
cm2
A(E) = Effective area
R(E, h) = Detector redistribution from energy E to channel h
E

## Slide 4: What Are Response Files?
E
Flux
E
cm2
Channel
CTS/S
C(h) = Counts in detector channel h
HEASARC
E

## Slide 5: What Are Response Files?
E
Flux
E
cm2
Channel
CTS/S
HEASARC
Ancillary response file: A(E) = Effective area
Redistribution matrix file: R(E) = Detector redistribution from energy E to channel h
E

## Slide 6: The ancillary response file (ARF)
The ARF contains the effective area as a function of energy. The ARF includes the geometric collecting area of the instrument multiplied by the energy-dependent efficiencies of:
mirrors
filters
detector
Energy (keV)
Effective Area (cm2)
XRISM effective area curves (point source)
Xtend
Resolve GVC

## Slide 7: The redistribution matrix file (RMF)
The RMF maps the relationship between the incident photon energy and the event’s pulse height. The RMF provides the probability that a photon of a given energy is registered in a given channel.
The width of the peak
gives the resolution
Xtend RMF
2 keV
4 keV
Energy (keV)
Counts/bin

## Slide 8: The redistribution matrix file (RMF)
Photopeak
Photopeak
Credits: Ogorzalek

## Slide 9: What Response Files are Provided for Cycle1?
Resolve Responses
  3 RMFs
  6 ARFs
Xtend Responses
  1 RMF
  2 ARFs
https://heasarc.gsfc.nasa.gov/docs/xrism/proposals/xrism_tools.html
XRISM Cycle 1 ARFs and RMFs will be available by early Feb
These files will be used for Webspec and Webpimms at the HEASARC web.
For both point and extended sources:

## Slide 10: Resolve RMFs
Pulse Height
Three event grade cases:
The proportion of events in the various event grades depends on the source count rate. At low rates, most events will achieve calorimeter resolution. For faint or moderately bright sources, rsl_Hp_5eV.rmf may be safely used for simulations.
100% of high-resolution events (Hp): rsl_Hp_5eV.rmf - FWHM of 5 eV
100% of mid-resolution events (Mp): rsl_Mp_6eV.rmf - FWHM of 6 eV
100% of low-resolution events (Lp): rsl_Lp_18eV.rmf - FWHM of 18 eV

## Slide 11: Resolve RMFs
Pulse Height
Three event grade cases:
But resolution is degraded for bright sources as mid-res and low-res events contribute more.
See Edmund’s talk.
100% of high-resolution events (Hp): rsl_Hp_5eV.rmf - FWHM of 5 eV
100% of mid-resolution events (Mp): rsl_Mp_6eV.rmf - FWHM of 6 eV
100% of low-resolution events (Lp): rsl_Lp_18eV.rmf - FWHM of 18 eV

## Slide 12: Resolve RMFs
Pulse Height
Three event grade cases:
NOTE:
The electron loss continuum is not included.
All 35 pixels have the same FWHM. See Francois’s talk for creating your own RMFs.
Eckart et al. 2018
HITOMI SXS
Electron loss
continuum
100% of high-resolution events (Hp): rsl_Hp_5eV.rmf - FWHM of 5 eV
100% of mid-resolution events (Mp): rsl_Mp_6eV.rmf - FWHM of 6 eV
100% of low-resolution events (Lp): rsl_Lp_18eV.rmf - FWHM of 18 eV

## Slide 13: Resolve ARFs - Gate Valve Closed
Two Source Types - 4 point and 2 extended cases
A point source at the Resolve aimpoint (but 15arcsec away from the optical axis) with the filter wheel open: rsl_standard_GVclosed.arf
A point source at the Resolve aimpoint with the Be filter: rsl_pointsource_fwBe_GVclosed.arf
A point source at the Resolve aimpoint with the ND filter: rsl_pointsource_fwND_GVclosed.arf
A point source at a ~1’ away from the aimpoint with the filter wheel open: rsl_pointsource_off_GVclosed.arf

## Slide 14: Resolve ARFs - Gate Valve Closed
Two Source Types - 4 point and 2 extended cases
A point source at the Resolve aimpoint (but 15arcsec away from the optical axis) with the filter wheel open: rsl_standard_GVclosed.arf
A point source at the Resolve aimpoint with the Be filter: rsl_pointsource_fwBe_GVclosed.arf
A point source at the Resolve aimpoint with the ND filter: rsl_pointsource_fwND_GVclosed.arf
A point source at a ~1’ away from the aimpoint with the filter wheel open: rsl_pointsource_off_GVclosed.arf
For bright sources:

## Slide 15: Resolve ARFs - Gate Valve Closed
Two Source Types - 4 point and 2 extended cases
Energy (keV)
Effective Area (cm2)
ND Filter
1’ offset
Standard
Be Filter

## Slide 16: Resolve ARFs - Gate Valve Closed
Two Source Types - 4 point and 2 extended cases
A 5’ radius source with flat distribution: rsl_extflat_GVclosed.arf
A 5.7’ radius source using a beta-model (rc = 1.26’ and β = 0.53). rsl_extbeta_GVclosed.arf
NOTE: At the aimpoint with the filter wheel open
See Francois’s talks and demos for creating your own arfs.
 | The fraction of simulated photons on Resolve FoV
Point source | 0.910
Flat circle | 0.232
Beta model | 0.467

## Slide 17: Resolve ARFs - Gate Valve Closed
Two Source Types - 4 point and 2 extended cases
At the aimpoint with the wheel filter open
Energy (keV)
Effective Area (cm2)
Flat
Beta

## Slide 18: Xtend ARFs and RMF
For both point and extended sources:
Xtend RMF - xtd_standard.rmf
2 Xtend ARFs
  A point source located at the aimpoint - xtd_standard.arf
  Flat circular distribution with a 5’ radius centered at the aimpoint - xtd_extflat.arf
This Xtend extended ARF does not reproduce the spatial / spectral complexity of any known extended source.
Point source
Xtend ARFs
5’ radius source

## Slide 19: These XRISM response files are:
available at the HEASARC XRISM web page: https://heasarc.gsfc.nasa.gov/docs/xrism/proposals/xrism_tools.html
adequate for spectral simulations for the Cycle 1 proposal preparations (not for the data analysis)
Caveats:
Some adjustments may be needed for the sources with spatial and spectral complexity.
HEASIM may need extra files (e.x. PSFs and vignetting), which will be eventually available but not by Feb 2024. HEASIM may need to use the HITOMI setup/files.
Resolve ARFs with GVO shall be available, if the gate valve is open and the NRA is revised.

## Slide 21: Xtend RMF
1
3
5
7
9
11
Xtend RMF
Energy (keV)
Counts/bin
Photon energy (keV)
Channel
Photopeak
Photopeak
2 keV
4 keV